## Slide 1: MDP -25 Mobile Data Power DC UPS
Operation Overview:
Motorola Application
With MW810 Computers & MVX 1000 Video Recorders

## Slide 2: Proper Voltage is the Life Blood of Mobile Data Transmitters
Mobile data transmitters and computers require stable and proper voltage input.
Low voltage or power loss causes system crashes, Lengthy reboot cycles, and potential software damage.

## Slide 3: Benefits
The MDP maintains voltage to critical electronics when vehicle voltage falters.
Internal back –up battery maintains DC output voltage during dips and black outs, Preventing memory loss and system crashes in mission critical mobile electronics.

## Slide 4: Motorola Application
Vehicle Battery
Shut Down Signal
DC Power
The MDP sends a signal initiating a low voltage shut down sequence in Motorola MW810 computers and VMX 1000 video recorders, preserving valuable data and the hard drive, and preventing the total discharge of the vehicle battery.
Output serial port provides low voltage signal when the input reaches 10 volts, allowing time for orderly shutdown before the low voltage disconnect activates.

## Slide 5: Application Example: Vehicle Engine Off, Electronics Running, Vehicle Battery Voltage Decay with MDP Activation
With Ignition Off
MDP senses when key ignition is turned off and sends shutdown signal to mobile computer, thus preserving both the MDP internal battery and vehicle battery.
With Ignition On
Internal back-up battery automatically switches online in 2 milliseconds when the vehicle’s battery voltage reaches approximately 10.0 VDC
When the internal battery is activated the MDP sends a shutdown signal to the mobile computer.
Figure 1: The MDP(orange) activates when the vehicle battery(blue) has dropped below 10VDC.
MDP Voltage to Mobile Computer
Vehicle Battery Voltage to Mobile Computer
Low Voltage Shutdown signal sent to the computer
10.0 VDC, MDP Battery Switches Online
If vehicle voltage is restored during the shutdown sequence, a power restore signal is sent, aborting the shutdown.
Notes: MDP under Vehicle

## Slide 6: Auto-Reconnect When Vehicle Alternator Restores Battery
  Vehicle battery auto-reconnects to the data transmitter when vehicle started and voltage reaches and maintains 11.5 VDC for 3 seconds, MDP battery goes offline and re-charges.
Figure 1: The MDP(orange) deactivates 3 seconds after the vehicle battery(blue) has been restored to 11.5+VDC .
Voltage Supplied by MDP to MDT
Vehicle Battery Recovers to 11.5 VDC
3 sec
MDP Disconnects
Vehicle Battery Voltage Switched on-line in parallel with MDP
MDT Voltage Fully Supplied by Vehicle Battery
Figure 1

## Slide 7: Sudden Voltage Drop During Engine Start-Up
Protects mobile computers against system crash preventing lengthy reboot sequence and a loss of data due to
  Voltage dip during engine cranking(figure 1)
Figure 1: The MDP(orange) maintains a voltage of 13.2V during a voltage dip(blue).
Figure 1
Sudden Battery Voltage Drop
MDP switches on and Maintains DC Power
Vehicle Battery

## Slide 8: Internal Battery Run Times
Power delivery @ > 10.2 volts @ 25°C
  5 amps @ 60 minutes
  10 amps @ 20 minutes
  25 amps @ 8 minutes

## Slide 9: Internal Battery Disconnect
Built-in LVD (Low Voltage Disconnect) activates at 8.9VDC; protecting the battery from complete discharge.

## Slide 10: Internal Battery Charging
Built-in, 3-Stage temperature compensated charging circuit maintains internal 8 Ah battery at full charge, ready to provide back-up power for an extended period.
Charging circuit operates on a vehicle battery input range of 10.5VDC to 14VDC.
The MDP Maintains the internal Battery at full charge
Vehicle Battery voltage drop over time
Vehicle Battery Drop is not linear.

## Slide 11: Other Features: Circuitry Protection
Graph Not To Scale
Overvoltage transient protection prevents damage to sensitive circuitry due to voltage line spikes.
Noise filter eliminates electronic noise and interference, providing clean power required by mobile electronics for proper operation.
As shown in figure 1 the MDP(Orange) continues to function after a voltage spike has occurred. The Noise filter also aids in creating a smooth curve by eliminating disturbances.
Spike in input battery voltage
MDP Functioning With the Spike

## Slide 12: Ease of Install
For Optimum Performance the MDP should be located within 24” of critical electronics.
The case does not require grounding so it can be installed on any surface material, in any orientation.
Input and output wiring is accomplished by using the lugs provided to connect the positive and negative leads of the power line or device to the positive and negative input and output terminals respectively.

## Slide 13: Ease of Battery Replacement
Disconnect the MDP Power, and turn off all loads and remove the fuse from the fuse holder labeled “BATTERY”.
Remove the front panel by loosening three screws.
The old battery may now be pulled out and a new battery can Inserted.
Typical battery life 5 years.

## Slide 14: Power Status Indicators
Power Status indicators provide visual system operational status/ troubleshooting.
  Top Green LED indicates the MDP is charging(Figure 1)
  Middle Amber LED indicates the MDP is supplying backup power.(Figure 2)
  Bottom green LED indicates input is connected(Figure 1)
Figure 1
Figure 2

## Slide 15: Built to Last
Conformal coated printed circuit board resists corrosion.
Rugged, rust and corrosion resistant powder coated aluminum case provides protection for components.
All components selected for dependable performance in hostile environments.
Two year limited warranty.