## Slide 1: MDP -25 Mobile Data Power DC UPS
Operation Overview
Non-Motorola Application

## Slide 2: Proper Voltage is the Life Blood of Mobile Data Transmitters
Mobile data transmitters and computers require stable and proper voltage input.
Low voltage or power loss causes system crashes, Lengthy reboot cycles, and potential software damage.

## Slide 3: Benefits
The MDP maintains voltage to critical electronics when vehicle voltage falters.
Internal back –up battery maintains DC output voltage during dips and black outs, Preventing memory loss and system crashes in mission critical mobile electronics.

## Slide 4: Non-Motorola Application Example:
Internal back-up battery automatically switches online in 2 milliseconds when the vehicle’s battery voltage reaches approximately 10.0 VDC.
  Note: External timer recommended to prevent discharge of vehicle battery. (see next slide)
Figure 1: The MDP(orange) activates when the vehicle battery(blue) has dropped below 10VDC.
MDP Voltage to Mobile Computer
Vehicle Battery Voltage to Mobile Computer
MDP Battery Low Voltage Disconnect Point 9.0VDC
10.0 VDC, MDP Battery Switches Online
Vehicle Battery
DC Power
Condition: Vehicle engine off, electronics running, vehicle battery voltage decay with MDP activation.
Notes: MDP under Vehicle

## Slide 5: Non-Motorola Application: Example With Power-off timer, TMR-30N, installed and ignition sense wire not connected
Vehicle Battery
TMR-30N
(Order Separately)
Before Engine Startup:
TMR-30N will not connect the load to the vehicle battery until the engine is started.
After Engine Shutdown:
Timer activates after sensing the engine stop and begins the time out sequence, disconnecting the mobile computer from the vehicle battery after the set interval, preventing the total discharge of the vehicle battery.
Internal back-up battery automatically switches online in 2 milliseconds when the vehicle’s battery voltage reaches approximately 10.0 VDC. If the battery voltage remains low for more than 3 seconds, the MDP will continue to Power the load until the vehicle battery is returned to 12VDC or greater or timer disconnects.

## Slide 6: Non-Motorola Application: Example With Power-off timer, TMR-30N, installed and ignition sense wire connected
With Ignition On
Timer will not activate until ignition is turned off.
Internal back-up battery automatically switches online in 2 milliseconds when the vehicle’s battery voltage reaches approximately 10.0 VDC.
If the vehicle battery decays to 10.0 volts prior to the timer disconnect, the MDP battery comes online and supplies power to the computer until it’s internal battery reaches 9.0 volts, and the LVD activates.
Ignition Switch
Vehicle Battery
TMR-30N
(Order Separately)

## Slide 7: Auto-Reconnect When Vehicle Alternator Restores Battery
  Vehicle battery auto-reconnects to the data transmitter when vehicle started and voltage reaches and maintains 11.5 VDC for 3 seconds, MDP battery goes offline and re-charges.
Figure 1: The MDP(orange) deactivates 3 seconds after the vehicle battery(blue) has been restored to 11.5+VDC .
Voltage Supplied by MDP to MDT
Vehicle Battery Recovers to 11.5 VDC
3 sec
MDP Disconnects
Vehicle Battery Voltage Switched on-line in parallel with MDP
MDT Voltage Fully Supplied by Vehicle Battery
Figure 1

## Slide 8: Sudden Voltage Drop During Engine Start-Up
Protects mobile computers against system crash preventing lengthy reboot sequence and a loss of data due to
  Voltage dip during engine cranking(figure 1)
Figure 1: The MDP(orange) maintains a voltage of 13.2V during a voltage dip(blue).
Figure 1
Sudden Battery Voltage Drop
MDP switches on and Maintains DC Power
Vehicle Battery

## Slide 9: Internal Battery Run Times
Power delivery @ > 10.2 volts @ 25°C
  5 amps @ 60 minutes
  10 amps @ 20 minutes
  25 amps @ 8 minutes

## Slide 10: Internal Battery Disconnect
Built-in LVD (Low Voltage Disconnect) activates at 8.9VDC; protecting the battery from complete discharge.

## Slide 11: Internal Battery Charging
Built-in, 3-Stage temperature compensated charging circuit maintains internal 8 Ah battery at full charge, ready to provide back-up power for an extended period.
Charging circuit operates on a vehicle battery input range of 10.5VDC to 14VDC.
The MDP Maintains the internal Battery at full charge
Vehicle Battery voltage drop over time
Vehicle Battery Drop is not linear.

## Slide 12: Other Features: Circuitry Protection
Graph Not To Scale
Overvoltage transient protection prevents damage to sensitive circuitry due to voltage line spikes.
Noise filter eliminates electronic noise and interference, providing clean power required by mobile electronics for proper operation.
As shown in figure 1 the MDP(Orange) continues to function after a voltage spike has occurred. The Noise filter also aids in creating a smooth curve by eliminating disturbances.
Spike in input battery voltage
MDP Functioning With the Spike

## Slide 13: Ease of Install
For Optimum Performance the MDP should be located within 24” of critical electronics.
The case does not require grounding so it can be installed on any surface material, in any orientation.
Input and output wiring is accomplished by using the lugs provided to connect the positive and negative leads of the power line or device to the positive and negative input and output terminals respectively.

## Slide 14: Ease of Battery Replacement
Disconnect the MDP Power, and turn off all loads and remove the fuse from the fuse holder labeled “BATTERY”.
Remove the front panel by loosening three screws.
The old battery may now be pulled out and a new battery can Inserted.
Typical battery life 5 years.

## Slide 15: Power Status Indicators
Power Status indicators provide visual system operational status/ troubleshooting.
  Top Green LED indicates the MDP is charging(Figure 1)
  Middle Amber LED indicates the MDP is supplying backup power.(Figure 2)
  Bottom green LED indicates input is connected(Figure 1)
Figure 1
Figure 2

## Slide 16: Built to Last
Conformal coated printed circuit board resists corrosion.
Rugged, rust and corrosion resistant powder coated aluminum case provides protection for components.
All components selected for dependable performance in hostile environments.
Two year limited warranty.