## Slide 1: TMR-30N Power Timer
Operation Overview

## Slide 2: Theory of Operations / Benefits
Model | Dimensions (Inches) |  |  | Weight (lbs)
 | H | W | D | 
TMR-30N | 1.25 | 4.25 | 2 | 1
Prevents discharge of vehicle batteries when vehicle electronics are left on.
In autosense mode (ignition sense wire disconnected) the timer senses the engine running and provides power to equipment. When the engine stops the TMR-30N begins the preset countdown to disconnect loads from the battery.
Compact size for easy installation in consoles:

## Slide 3: Ease of Installation
Simple installation:
  Power in from battery
  (30A fuse provided)
  Power out to loads
  Chassis ground
After power off timer has activated, power to auxiliary circuits is automatically restored when the engine is started.
Power In from battery
Chassis Ground
Ignition Sense (Optional)
Power to Loads

## Slide 4: Ignition Sense Capability
If the ORANGE wire is connected to a circuit that is hot when the ignition switch is on, your equipment will come on immediately with the ignition.
This configuration is recommended for emergency service vehicles to guarantee equipment operation in critical situations.
Upon turning the ignition switch off the TMR-30N countdown sequence will begin.

## Slide 5: Easily Programmable Disconnect Time Limit
  15min to 8hr programmable dip switch
  Ability to match your auxiliary load use to battery capacity
  Ensures maximum run time while saving reserve for engine start.
DIP Switch |  |  |  | Time Setting
1 | 2 | 3 | 4 | 
Off | Off | Off | Off | 6 min.
Off | Off | Off | On | 15 min.
Off | On | Off | Off | 18 min.
On | Off | Off | Off | 24 min.
Off | Off | On | Off | 30 min.
Off | On | Off | On | 45 min.
On | Off | Off | On | 1 hr.
Off | On | On | Off | 1.5 hr.
On | Off | On | Off | 2 hr.
Off | On | On | On | 3 hr.
On | On | ON | Off | 4 hr.
On | On | On | On | 5 hr.

## Slide 6: Programming Example
The TMR-30N can be integrated with any vehicle electronics.
Step 1: Select and set the desired time out interval based on intended use of vehicle accessories while engine is off.
  Factors to consider are total load, battery capacity, and maximum depth of discharge necessary to ensure excess power to restart the engine.
Step 2: Test the time out sequence and vehicle battery condition at set timeout duration.
  Adjust timer duration if necessary.
    Note: extended time out periods may fully discharge vehicle battery , so some experimentation may be necessary for your particular vehicle loads and battery capacity.

## Slide 7: LED Output Status Indicators
LED | Description
Solid Green | Output Power OK, Timer Off
Flashing Green | Output Power OK, Timer On
Solid Red | No Output Power, Timed Out
Flashing Red | No Output Power, Low Voltage
Two LED’s constantly alert the user to the output status of the timer.

## Slide 8: High Current Rating
  30 amp rating allows multiple auxiliary loads / circuits to be powered at once.
  Radios
  MDT
  Panasonic Toughbook
  Allows many critical electronics to be left on during emergency calls without running the engine and preserves the battery for restart.

## Slide 9: High and Low Voltage Protections
  Low voltage disconnect below 10.5V after a 10 second delay to avoid nuisance tripping.
Chart: High Voltage Disconnect
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 10.8 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15
Power Out | 16.25 | 16.2667 | 16.2833 | 16.3 | 16.3167 | 16.3333 | 16.35 | 16.3667 | 16.3833 | 16.4 | 16.4167 | 16.4333 | 16.45 | 16.4667 | 16.4833 | 16.5 | 16.5167 | 16.5333 | 16.55 | 16.5667 | 16.5833 | 16.6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Power In | 16.25 | 16.2667 | 16.2833 | 16.3 | 16.3167 | 16.3333 | 16.35 | 16.3667 | 16.3833 | 16.4 | 16.4167 | 16.4333 | 16.45 | 16.4667 | 16.4833 | 16.5 | 16.5167 | 16.5333 | 16.55 | 16.5667 | 16.5833 | 16.6 | 16.61 | 16.6167 | 16.6333 | 16.65 | 16.6667 | 16.6833 | 16.7 | 16.7167 | 16.7333 | 16.75
Chart: Low Voltage Disconnect
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15
Power Out | 10.6 | 10.58 | 10.56 | 10.54 | 10.52 | 10.5 | 10.48 | 10.46 | 10.44 | 10.42 | 10.4 | 10.38 | 10.36 | 10.34 | 10.32 | 10.3 | 10.28 | 10.26 | 10.24 | 10.22 | 10.2 | 10.18 | 10.16 | 10.14 | 10.12 | 10.1 | 0 | 0 | 0 | 0 | 0
Power In | 10.6 | 10.58 | 10.56 | 10.54 | 10.52 | 10.5 | 10.48 | 10.46 | 10.44 | 10.42 | 10.4 | 10.38 | 10.36 | 10.34 | 10.32 | 10.3 | 10.28 | 10.26 | 10.24 | 10.22 | 10.2 | 10.18 | 10.16 | 10.14 | 10.12 | 10.1 | 10.1 | 10.1 | 10.1 | 10.1 | 10.1
  High voltage disconnect activates above 16.5V for 3 seconds.
Power to Loads
Vehicle Voltage
Vehicle Voltage
Power to Loads
High Voltage Sense Point
Low voltage cut-off sense point
High Voltage Disconnect
Low voltage disconnect

## Slide 10: Design Features
Waterproof timeout setting switches.
Designed to withstand engine compartment vibration and perform in demanding emergency vehicle applications.
Powder coated steel with epoxy potted components
Operating Temp: -4oF to 176oF
Low standby current: 13mA